Private Pilot Solo Requirements (CFR 61.87)

Administrative:

Note: Special process required for Students training on a visa

- Student Pilot Certificate  (IACRA)

- Third Class Medical Certificate (Aviation Medical Examiner)

- SFRA Online Training (Print Card)

https://www.faasafety.gov/gslac/ALC/courseLanding.aspx?cID=405

- TSA Online Training (Recommended)

http://flash.aopa.org/asf/gasecurity/gasecurity.cfm?

Aeronautical Knowledge:

- Pre-solo test (open book)

Flight Proficiency:

- Flight Preparations

  - PreFlight Planning

  - Power Plant Operations

  - Aircraft Systems

- Taxiing and Run-up

- Normal Take-off and Landings

Cross-wind Take-off and Landings

- Straight and Level Flight; Turns in Both Directions

- Climbs and Climbing Turns

- Airport Traffic Pattern- Entries and Departures

- Collision Avoidance

Wake Turbulence Avoidance

Windshear Avoidance

- Descents- with and without turns

In both high and low drag configurations

- Flight at various airspeeds from cruise to slow flight

- Stall Entries from various flight attitudes & power combinations with recovery

- At first indication of a stall

- From full stall

- Emergency Procedures and Equipment Malfunctions

- Ground Reference maneuvers

- Approach to a landing area with simulated engine malfunction

- Slips to a landing

- Go-Arounds